## Slide 1: GDB Tool for ADSP Guide

## Slide 2: Agenda
Environment Setting
User Guide
[Options] SYS_ADSP_DUMP Memory Layout
Trouble Shooting

## Slide 3: Agenda
Environment Setting
User Guide
[Options] SYS_ADSP_DUMP Memory Layout
Trouble Shooting

## Slide 4: Environment Setting
Requirement:
  You “MUST” install Python 3 on Linux server, otherwise the python script would be fail.
  You “MUST” get the XtensaTool which download from cadence.
  You “MUST” get the license key for using XtensaTool
  You “MUST” copy TOOL/GDB_DEBUG/hifi_debug_vXpX.tar.xz to your Linux Server from Aurisys package

## Slide 5: Download XtensaTools from IDE

## Slide 6: Set License Key
Please export the License Server Address before using the tool
  export XTENSAD_LICENSE_FILE=‘<port>@<server>'

## Slide 7: Tar hifi_debug_vXpX.tar.xz on server
Decompress the Tool to linux server
  tar Jxvf hifi_debug_tool_vXpX.tar.xz
!!! copy XtensaTool which download from cadence !!!

## Slide 8: Auto setup by tool_setup.sh
./tool_setup.sh
  Show tools support information
./tool_setup.sh RI-2021.8
  Ex: mt6985 is RI-2021.8, tool setup to RI-2021.8
  Create soft link as previous folder structure
  Fast-switch different xtensatools version by the script

## Slide 9: Folder Structure (after tool_setup.sh)
Tool script for adsp debug
Hwcfg copy from aurisys package
XtensaTool from cadance
Soft link to XtensaTools path
Soft link to hwcfg path

## Slide 10: Copy params files to XtensaTools/config
Copy params files to related version of XtensaTools/config
Copy params files to related version of XtensaTools/config
“Auto copy after hifi_debug_v5p3”

## Slide 11: Agenda
Environment Setting
User Guide
[Options] SYS_ADSP_DUMP Memory Layout
Trouble Shooting

## Slide 12: Simple usage
cd hifi_debug/adsp_debug_tool
Put the correspond hifiX_X.elf and SYS_ADSP_DUMP
./debug_adsp.sh ${platform} ${elf_path}
Ex
  ./debug_adsp.sh mt6983 hifi3_a.elf ;# debug mt6983 hifi a
  ./debug_adsp.sh mt6983 hifi3_b.elf ;# debug mt6983 hifi b
  ./debug_adsp.sh mt6985 hifi5_a.elf ;# debug mt6985 hifi a
  ./debug_adsp.sh mt6985 hifi5_b.elf ;# debug mt6985 hifi b

## Slide 13: Simple usage

## Slide 14: Examining the Stack

## Slide 15: Examining the Data

## Slide 16: Examining the Memory

## Slide 17: Examining Source Files or Assemble code

## Slide 18: Switch to other task and show backtrace

## Slide 19: Agenda
Environment Setting
User Guide
[Options] SYS_ADSP_DUMP Memory Layout
Trouble Shooting

## Slide 20: [Options] SYS_ADSP_DUMP layout
Mt6985, Mt6886 :
  Parse by dump header & elf
Others legacy platform
  Parse by Config.ini
Need to update “config.ini” if memory relayout

## Slide 21: [Options 1] Parse by dump header
Magic: 0xAD5BAD5B | Size: 0x6000 | Name: cfg
Mem dump |  | 
Magic: 0xAD5BAD5B | Size: 0x5000 | Name: cfg2
Mem dump |  | 
Magic: 0xAD5BAD5B | Size: 0x9000 | Name: itcm
Mem dump |  | 
Magic: 0xAD5BAD5B | Size: 0x8000 | Name: dtcm
Mem dump |  | 
Magic: 0xAD5BAD5B | Size: 0x900000 | Name: sysram
Mem dump |  | 
……
SYS_ADSP_DUMP Binary Layout

## Slide 22: [Options 1] Parse by dump header (2)
gdb_cmd.txt
Parse section address by reading specific symbol from elf file

## Slide 23: [Options 2] Parse by Config.ini
Mem dump
Mem dump
Mem dump
Mem dump
Mem dump
……
SYS_ADSP_DUMP Binary Layout
./debug_adsp.sh mt6885 hifi3_a.elf
SYS_ADSP_DUMP
sequence
File: ./python3/Config.ini
CFG_HIFI3_SRAM_SIZE = SYS_DRAM: should be the same configuration at platform.mk
[Remind] Generally if Memory optimization or increase heap, you must change the debug layout

## Slide 24: (cont.)[Options 2] SYS_ADSP_DUMP Layout
Version | V1 |  | V2 |  | V3 |  | V4 | 
Platform [Android Version] | mt6779 mt6785 [Q] |  | mt6885 mt6873 mt6893 |  | mt6853 mt6877 |  | mt6785 [R] mt6781 | 
File Size (Around) | 14 MB |  | 8 MB |  | 10 MB |  | 8 MB | 
Layout | Segment | Size | Segment | Size | Segment | Size | Segment | Size
 | ELF Header | 8 KB | CFG_REG | 24 KB | CFG_REG | 24 KB | CFG_REG | 64 KB
 | ITCM | 36 KB | ITCM | 36 KB | ITCM | 36 KB | ITCM | 36 KB
 | DTCM | 32 KB | DTCM | 32 KB | DTCM | 32 KB | DTCM | 32 KB
 | Temp | 288 B | SYS_DRAM | 7 MB | SYS_DRAM | 9 MB | SYS_DRAM | 7 MB
 | CFG_REG | 64 KB | CoreDump | 1 KB | CoreDump | 1 KB | CoreDump | 1 KB
 | SYS_DRAM | 7 MB | LOG_A | 512 KB | LOG_A | 512 KB | LOG_A | 512 KB
 | CoreDump | 1 KB | LOG_B | 512 KB | LOG_B | 512 KB | LOG_B | 512 KB
 | IPI_Buffer | 5 MB |  |  |  |  |  | 
 | LOG | 2 MB |  |  |  |  |  | 
 | Reserved Memory *mt6779 only | 9 MB |  |  |  |  |  | 
…….

## Slide 25: Agenda
Environment Setting
User Guide
[Options] SYS_ADSP_DUMP Memory Layout
Trouble Shooting

## Slide 26: Error: param file not in config folder
Ans : Copy params files to XtensaTools/config

## Slide 27: Error: Configparser.NoSectionError
Ans: [Options 2] Parse by Config.ini
Need add the platform layout of mtxxxx_x

## Slide 28: Error: could not load ISA
The mtxxxx-params path setting is wrong

## Slide 29: (cont.) Error: could not load ISA
Example: mtXXXX-params
  Fix hwcfg relative paths to the location of this file (XtensaTools/config/mtxxxx-params)
Correct
Wrong

## Slide 30: Error: could not load ISA – port error
Ping Specific Port using telnet:
$ telnet <ip_address> <port_number>
$ telnet <domain_name> <port_number>
If can’t ping the license server, please check the firewall setting or contact to IT for help
Ref: Set License Key