## Slide 1
AudioDSP C++ Library Guideline
MediaTek

## Slide 2: Outline
Local build C++ lib
How-to build-in in ADSP image
Add library to scenario
Limitation and notes
Appendix
  ARSI-PROC APIs
  ARSI-PAR APIs
C++ demo lib

## Slide 3: Flow
By IDE
By linux cmd
Local prebuild library
(choose either one)
HWCFG
Toolchain
Source code
Preparation
.a file
Add to scenarios
Output library file
Build-in in ADSP image
Notes: Example: CL#4584600; 4584636; 4584718

## Slide 4: Local build C++ lib – Environment Settings
Path: /vendor/mediatek/proprietary/tinysys/common/drivers/audio/aurisys/lib/democpp/
File Name | Description
DemoCpp.cpp | Your cpp source code
DemoCpp.h | Your header file
democpp_wrapper.cpp | ARSI-PROC APIs. Please rename function prefix to your library name! (ex. democpp_arsi_query_working_buf_size to xxx_arsi_query_working_buf_size)
democpp_wrapper_private_type.h | Define API related struct
Makefile | 
README | -
Var | Description | Example
Platform | platform | mt6989_a
XT_TOOLS_VERSION | toolchain version | RI-2023.11-linux
XT_TOOLS_BIN_DIR | toolchain path | $(ALPS_PATH)/prebuilts/clang/xtensa/linux-x86/$(XT_TOOLS_VERSION)/XtensaTools/bin
INSTALLDIR | the actual path where the library is called | $(ALPS_PATH)/vendor/mediatek/proprietary/tinysys/adsp/HIFI5_SP/middleware/lib/$(XT_TOOLS_VERSION)/libdemocpp
CC | compiler (xcc/clang) | $(ADSP_CROSS_COMPILE)xt-clang++
OUT_FILES | output library name | libdemocpp.a
libdemocpp.a | modify $(OBJ_FILES) target to your library name | 
For API details, please refer to Aurisys API - arsi_api.h

## Slide 5: Local build C++ lib – Command & Output
Command: $make clean; make
Output:
  The output library will be in the same folder path
    Ex. /vendor/mediatek/proprietary/tinysys/common/drivers/audio/aurisys/lib/democpp/libdemocpp.a
  Makefile will help copy library to the actual path where the library is called
    Ex. /vendor/mediatek/proprietary/tinysys/adsp/HIFI5_SP/middleware/lib/RI-2023.11-linux/libdemocpp/libdemocpp.a
copy

## Slide 6: How-to build-in in ADSP image
Check Link scripts:
  *lib: -lc -lgloss -lminrt -lc -lhandler-reset -lhandlers-board -lminrt -lhal -lc -lstdc++
    Path: /vendor/mediatek/proprietary/tinysys/adsp/HIFIX_SP/project/mt6xxx/HIFIX_A/platform/lnk-hifiX/RI-20XX.X-linux/specs
Config (under platform.mk)
  Library entry config
    Example
      CFLAGS += -DAURISYS_CPP_SUPPORT
  LIBFLAGS
    Assume the prebuilt library is libxxx.a
      LIBFLAGS += -Wl,-L$(ADSP_MIDDLEWARE_DIR)/lib/$(XT_INTERNAL_LIB_DIR)/lib_folder_name -lxxx
    Example
      LIBFLAGS += -Wl,-L$(ADSP_MIDDLEWARE_DIR)/lib/$(XT_INTERNAL_LIB_DIR)/libdemocpp -ldemocpp
To distinguish this
arsi_library_entry_points.h
Notes: Example patch: CL#4584636

## Slide 7: Add library to scenario
Please refer to AudioDSP_Development_Tutorial.doc - New Aurisys Scenario for details!!!
Example:
Check adsp log
1
2
3
Add library to:
- Scenario (as shown in
the picture on the right)
- DVFS
- Aurisys library entry
Confirm the query
result is as expected
Scenario
Lib name
Lib version
Notes: Example patch: CL#4584718

## Slide 8: Limitation and notes
There are some functions (APIs) must be implemented
  Please check ARSI-PROC APIs & ARSI-PAR APIs (the red ones in Appendix)
    ARSI-PROC APIs: demolib examples are in democpp_wrapper.cpp

## Slide 9: [Appendix] ARSI-PROC APIs
Functions | Description
arsi_query_working_buf_size | Query the size of the working buffer
arsi_query_process_unit_bytes | Query the basic data consumption for uplink/downlink processing
arsi_create_handler | Create handler and initialize it
arsi_process_ul_buf | Processing microphone/uplink data
arsi_process_dl_buf | Processing playback/downlink data
arsi_destroy_handler | De-initialize handler and destroy it (no need to free the working buffer)
arsi_update_device | Update task device info
arsi_update_param | Update enhancement parameters
arsi_set_ul_digital_gain | Set uplink digital gain
arsi_set_dl_digital_gain | Set downlink digital gain
arsi_set_ul_mute | Mute/unmute uplink
arsi_set_dl_mute | Mute/unmute downlink
arsi_set_ul_enhance | Enable/disable uplink enhancement function
arsi_set_dl_enhance | Enable/disable downlink enhancement function
arsi_set_debug_log_fp | Set debug log print callback function
arsi_query_max_debug_dump_buf_size | Query the size of dump buf file for each downlink/uplink processing
arsi_set_addr_value | Set value at a specified address
arsi_get_addr_value | Get value from the specified address
arsi_set_key_value_pair | set key_value string to library
arsi_get_key_value_pair | get key_value string from library

## Slide 10: [Appendix] ARSI-PAR APIs
Functions | Description
arsi_load_param | This function will only called once when device boot up. Load the parameter file content into memory Library can retrieve the parameter buffer from memory without any file I/O afterward Implemented in AP side only, but not in DSP.
arsi_query_param_buf_size_by_custom_info | Query the buffer size to keep speech enhancement parameters Implemented in AP side only
arsi_parsing_param_file_by_custom_info | Parsing param file to get parameters into p_param_buf Implemented in AP side only

## Slide 11: C++ Demo Lib
Find cpp demo lib under Aurisys package or ALPS codebase
  Aurisys path: Aurisys_exe_V1.XXXX.01\DOC\adsp_lib_guideline
  ALPS path: alps/vendor/mediatek/proprietary/tinysys/common/drivers/audio/aurisys/lib/democpp/

## Slide 12
Thank you
Questions and Discussions