## Slide 1: Hifi3 Debugging Tools
2019/1/7

## Slide 2: Debug Items
Basic function
  UART (useful!)
  Logger (useful!)
  CFGREG Dump
  ADSP JTAG
System SW debug
  Monitor
    Task monitor (useful!)
    Heap Management Tool
    Timestamps
  Assert
    Exception Handler (useful!)
    Stack overflow / Malloc failed hook
  Dump
    TRAX
    XT-GDB Dump (useful!)
    Debug Dump type (useful!)
    Debug Command (useful!)
System img debug
  xt-objdump
Audio Related
  Audio PCM Dump (useful!)
  Audio Utilities
    HEAP : AUDIO_CHECK(ptr)
    LOCK : MTK_AUDIO_LOCK_ENABLE_TRACE
    AUDIO IPI : print_msg_info
    IPI DMA : DUMP_REGION
    RINGBUF SW: DUMP_RINGBUG
    RINGBUF HW dump function

## Slide 3: Basic function
Uart
  uart2 : 921600
  CFG_UART_SUPPORT = yes (default =no for performance)
  align kernel timestamp
    CFG_KERNEL_TIMESTAMP_SUPPORT =yes
  print AP suspend info
    use freeRTOS tick to continue timestamp, timestamp will retrograde after AP resume.

## Slide 4
Uart
With printf function, AUD_LOG_V will not print log
Runtime disable/enable uart output (ADSP should be active to received command)
adb shell "echo 1 > /sys/class/misc/adsp/adsp_uart_switch"
adb shell "echo 0 > /sys/class/misc/adsp/adsp_uart_switch"
System print | Audio Feature print
PRINTF_D | AUD_LOG_D
PRINTF_I | AUD_LOG_I
PRINTF_W | AUD_LOG_W
PRINTF_E | AUD_LOG_E

## Slide 5
ADSP Logger
  Linked in MTKlogger
  /sdcard/mtklog/mobilelog/adsp_log_xxx_
ADSP EE log
  Triggered by user cmd
    /sys/class/misc/adsp # cat adsp_A_db_test
  Triggered by system exception (EE & Kernel API)
    SYS_ADSP_DUMP in db file
ELF header | ITCM | DTCM | reserved | hifi3 cfgreg | dram(system) | hifi3 core reg | Dram (shared mem)
SYS_ADSP_DUMP composition

## Slide 6
ADSP EE Format
  "aud_pla": the name of Hifi3 task in which exception is happened.
  If the exception is caused by ASSERT, the filename and line information will be shown in aee screen and __exp_main.txt in db.
  SYS_ADSP_DUMP can see the ADSP Last Log

## Slide 7
ADSP CFGREG dump
Runtime check Hifi3 config register
  adb shell cat /sys/class/misc/adsp/adsp_A_reg_status
All the Hifi3 config register will be dumped
to SYS_ADSP_DUMP in aee db file when
AEE exception is triggered by Hifi3 WDT.

## Slide 8
ADSP JTAG (Currently only available at EVB board )
JTAG HW setup (Use Flyswatter2 as ADSP JTAG)
  EVB need Rework, please find corresponding SA
  Set GPIO to ADSP_JTAG Mode for JTAG
Notes: OCD manager 找不到controller : hifi3 CPU reset需要放掉

## Slide 9
JTAG SW setup
  Xplorer Download and installed Xtensa OCD Daemon 12.0.6
  Set Debug Target Configuration

## Slide 10
  Set Debug Configuration

## Slide 11
  Debug window

## Slide 12: System SW debug
  TASK Monitor
    Total Heap status
    Task status
      State
    'B' - Blocked
    'R' - Ready
    'D' - Deleted (waiting clean up)
    'S' - Suspended, or Blocked without a timeout
          Stack
    The lower number the less free space.
Notes: 'B' - Blocked
'R' - Ready
'D' - Deleted (waiting clean up)
'S' - Suspended, or Blocked without a timeout

## Slide 13
Heap Memory Management Tool
Extend from FreeRTOS (heap_4.c only)
Feature 1: Monitor heap memory usage
  Combine Task Monitor, Monitor each time slice memory usage.
Feature 2 : Detail information of allocate memory
  Command, dump detail information of each allocate block

## Slide 14: Feature 1: Monitor heap memory usage
#define configUSE_MALLOC_MEMORY_USAGE (FreeRTOSConfig.h)
Audio is playing
Audio stop (idle)
Heap usage by each task

## Slide 15: Feature 2: Detail information of allocate memory
Triggered in vApplicationMallocFailedHook
  Need combined with Feature 1 (both set in FreeRTOSConfig.h)
#define configUSE_MALLOC_DEBUG_MSG_LEN 32
Memory header point
size
task
File : line

## Slide 16
  TimeStamps
    IPI
      CFG_IPI_STAMP_SUPPORT
      Record each ipi id send/recv success count
    IRQ
      set_irq_limit(1)  default 3 ms, if over threshold, print error msg
    Task function process
      Audio_task_utility
        init_time_interval(int id, unsigned long long thresholdns)
        record_time_interval(int id);  warning if the function process time over thresholdns.
        stop_time_interval(int id);

## Slide 17
  Exception Handler
    Through ADSP Uart
    Dump stack register
      Feed in Xt-gdb to trace
    Exception cause and address
      epc
      exccause
      excvaddr
Notes: The program counter (PC) holds the address of the next instruction to execute
PS : processor state

## Slide 18
Malloc Failed
  vApplicationMallocFailedHook(void)
Stack overflow
  vApplicationStackOverflowHook(xTaskHandle pxTask, char *pcTaskName)
  Check when Task context switch
  Can reference on Task Monitor Stack status
Above Errors will trigger system Assert (WDT) to info AP

## Slide 19
TRAX
  Xtensa provided, record function execution flow (no data info)
TRAX enable method :
  adb cmd
    AP sends IPI_TRAX_ENABLE to trigger DSP enable/disable TRAX.
  cd sys/class/misc/adsp
    echo 1 > adsp_A_trax. (start record)
    echo 0 > adsp_A_trax. (stop record)
    cat adsp_A_trax

## Slide 20: Analyze trace data by Xplorer (0)

## Slide 23
GDB DUMP (Useful to debug!)
  Use AEE db file to show more debug info
Get Tools: (version 3.0 , for mt6779 only)
  Aurisys_exe_Vxxxxxxx\TOOL\HiFi3
decompress the tools to the linux server
  tar -jxv -f hifi3_debug_tool_v3_181217.tar.bz2
add tools path to the bashrc
  vim .bashrc
  export PATH=$PATH:/proj/mtkxxxx/hifi3_debug_tool/XtensaTools/bin

## Slide 24
Preparation : Put files into the hifi3_debug_tool folder
  SYS_ADSP_DUMP : decompress the db file, copy out the "SYS_ADSP_DUMP"
    ex: TagLog_2010_0101_001217_EE\db.01.EE\20180511_172021_386\db.01.EE.dbg.DEC\SYS_ADSP_DUMP
  hifi3_a.elf : which is in the out folder, copy it out too.
    partial_build :
    $(alps)\vendor\mediatek\proprietary\tinysys\freertos\source\tinysys-scp_out\freertos\source\HIFI3_A\hifi3_a.elf
    full_build :
    $(alps)\out\target\product\$(project)\obj\TINYSYS_OBJ\tinysys-adsp_intermediates\freertos\source\HIFI3_A\hifi3_a.elf
    Official load :
    \ALPS_symbols\{branch name}\ {branch tag}\{project}.out.symbols\alps\out\target\product\{project}\obj\TINYSYS_OBJ

## Slide 25
Basic CMD
  python XtensaTools/bin/split_coredump SYS_ADSP_DUMP
  xt-gdb
  (xt-gdb) source script.txt
(Optional) ADSP Boot up exception
  Check the stack address: (0x4ffb0d70 is just example here)
  Log or Uart :
    Key word : "[8.342](A) Stack Dump address: 0x4ffb0d70"
  Xt-gdb
    (xt-gdb) print pExceptionContext
    $1 = (ExceptionContext *) 0x4ffb0d70 <exceptionContext_109>
  Use split_coredump with parameter of address at register file
    split_coredump SYS_ADSP_DUMP 0x4ffb0d70
GDB Split contents
  DTCM : Internal data memory
  ITCM: Internal code memory
  CFG_REG : Config register dump
  Log : last log for debug
  Register : hifi3 core registers.
  SYS_Dram : for system memory

## Slide 26
Basic GDB cmd for back trace, other gdb cmd please use help to check
$ python split_coredump SYS_ADSP_DUMP
$ xt-gdb
$ (xt-gdb) source script.txt
$ (xt-gdb) Info threads
$ (xt-gdb) thread n
$ (xt-gdb) bt
[Customer Notice]
Thread-info supported after RG-2018.9
If the version before RG-2018.9 , do the below flow.[N1]
Notes: [N1] If the version before RG-2018.9 , do the below flow.
In the path “\RG-2018.9-win32\XtensaTools\share\gdb\python”, copy folder FreeRTOS to the folder
“\RG-2017.6-win32\XtensaTools\share\gdb\python”.
From the folder “C:\usr\xtensa\XtDevTools\install\tools\RG-2018.9-win32\XtensaTools\share\gdb\python\thread_aware_rtos”, copy the file __init__.py and replace the same file in folder “C:\usr\xtensa\XtDevTools\install\tools\RG-2017.6-win32\XtensaTools\share\gdb\python\thread_aware_rtos”.
Run the xt-gdb session again.

## Slide 27: GDB Dump

## Slide 28: Debug Dump type
Dump type | Hifi3 in Exception (EE) | Kernel API | KE reboot | HW reboot
CFG reg | Y | Y | Y | N
I/D TCM | Y | Y | Y | Y
Core Register | Y | ? | N | N
Dram | Y | Y | N | N
Debug Tool | Xt-gdb | Xt-gdb | Check CFG reg Check ITCM Check DTCM | Check ITCM Check DTCM
Version | Legacy | Legacy | From p0.mp3.p60 | From p0.mp3.p74
FileName | SYS_ADSP_DUMP | SYS_ADSP_DUMP | SYS_EXTRA_ADSP_RAW | SYS_ADSP_COREDUMP

## Slide 29: Debug method
Xt-gdb: (with split_coredump)
  Backtrace(if no core register dump, useless), View all data , adsp log
Check CFG reg
  PC & SP & IRQ & Internal CLK CG & exception addr & cause & BUS monitor info.
Check ITCM
  Check the instruction memory whether occur memory corruption?
Check DTCM
  ADSP_A_OSTIMER_BUFFER (ADSP_A_DTCM_SHARE_BASE - 0x0040)
    Check current Ostimer time
  ADSP_A_IPC_BUFFER (ADSP_A_DTCM_SHARE_BASE - 0x0280)
    Check ipi last send/recv to share buffer
  ADSP_A_SYS_STATUS (ADSP_A_DTCM_SHARE_BASE - 0x0688)
    Check hifi status (reset, sleep, suspend, active) USEFUL!
  ADSP_BUS_MON_BACKUP_BASE (ADSP_A_DTCM_SHARE_BASE - 0x0744)
    Check whether occur bus hang & latched R/W addr
  ADSP_INFRA_BUS_DUMP_BASE (ADSP_A_DTCM_SHARE_BASE - 0x07E4)
    Check whether occur infra bus hang

## Slide 30: Debug Command
These command can help you to dump some adsp system message or do some profiling
Before use debug command, you need to check the "CFG_DEBUG_COMMAND_SUPPORT = yes" in adsp platform.mk
Write the command to adsp
  adb shell "echo %command% %variable% > sys/kernel/debug/audiodsp“
  Ex:
  adb shell "echo cmds > sys/kernel/debug/audiodsp“
Read the result in the memory and show it on user space
  adb shell "cat sys/kernel/debug/audiodsp”

## Slide 31
Class | %command% | %variable% | Help | Result in memory
help | cmds | N | show the support commands (some of command isn't support with compile option) | Y
dvfs | dvfs_dump | N | show the system feature/swip mcps information show the dvfs (vore, ddr_rate, cpu freq) information | Y
Task monitor | task_monitor_start | [option] time_ms | start or re-start task monitor with time_ms, it can change the task monitor period (>=50ms) | N
 | task_monitor_stop | N | stop task monitor | N
 | task_monitor_dump | N | show the task monitor result in user space | Y
Trace | trace_start | N | start trace the event when task context switch | N
 | trace_stop | N | stop trace function and show the result | Y

## Slide 32: System img debug
Get HiFi3 Assembly Code From Object File
  Use the "xt-objdump.exe" tool.
  Tool path: D:\usr\xtensa\XtDevTools\install\tools\RG-2017.6-win32\XtensaTools\bin
Command : (you can try other flag to gain more info from obj file, xt-objdump --help )
  xt-objdump.exe --xtensa-core=hifi3_xxx -d "object file name" > "assembly code file name"
  example: xt-objdump.exe --xtensa-core=hifi3 -d bqriirf_df1_hifi3.o > bqriirf_df1_hifi3_asm.txt
Notes:   Buf Address need 128byte aligned

## Slide 33: Audio Related Debug
Audio PCM DUMP
  Enable/Disable method
    adb shell setprop vendor.streamout.dsp.dump 1
    adb shell setprop vendor.streamout.dsp.dump 0
  Use IPI + dma to transfer data back
Dump file position
  / data/vendor/audiohal/audio_dump/
driver implement code
Notes:   Buf Address need 128byte aligned

## Slide 34
HEAP :
  AUDIO_MALLOC(sz)
  AUDIO_CHECK(ptr)
  AUDIO_FREE(ptr)
LOCK :
  MTK_AUDIO_LOCK_ENABLE_TRACE (Local config)
size
0x55
0x66
pxNextFreeBlock
p_head
p_tail
Check head & tail value
[132.141](A) [E][ALOCK] 0x6a088700: lock((mAurisysLibManagerLock), 1000), audio_task_audplayback.c, CreateAurisysLibManager(), 691L FAIL!! retval: 4294966221, try to lock when [131.141]
[132.143](A) [E][ALOCK] 0x6a088700:
========================= dump(+) =========================
[132.144](A) [E][ALOCK] 0x6a088700: time [131.141], lock((mAurisysLibManagerLock)), audio_task_audplayback.c, CreateAurisysLibManager(), 688L
[132.145](A) [E][ALOCK] 0x6a088700:
========================= dump(-) =========================
[132.146](A) AUD_WARNING(lock timeout!!): "drivers/common/audio/tasks/audplayback/audio_task_audplayback.c", 691L
[132.147](A) [ASSERT]task:aud_pla,file:drivers/common/audio/tasks/audplayback/audio_task_audplayback.c,line:691
First place to acquire lock
Notes: enum { /* audio_ipi_msg_data_t */
AUDIO_IPI_MSG_ONLY,
AUDIO_IPI_PAYLOAD,
AUDIO_IPI_DMA,
};
enum { /* audio_ipi_msg_ack_t */
/* bypass ack, but still send to audio queue */
AUDIO_IPI_MSG_BYPASS_ACK = 0,
/* need ack, and block in audio queue until ack back */
AUDIO_IPI_MSG_NEED_ACK = 1,
AUDIO_IPI_MSG_ACK_BACK = 2,
/* bypass audio queue, but still send to ipc queue */
AUDIO_IPI_MSG_DIRECT_SEND = 3,
AUDIO_IPI_MSG_CANCELED = 8
};

## Slide 35
AUDIO IPI :
  void print_msg_info(const char *func_name, const char *description, const struct ipi_msg_t *p_ipi_msg);
  audio_send_ipi_msg_to_kernel()
    Print ipi msg when send fail
Notes: enum { /* audio_ipi_msg_data_t */
AUDIO_IPI_MSG_ONLY,
AUDIO_IPI_PAYLOAD,
AUDIO_IPI_DMA,
};
enum { /* audio_ipi_msg_ack_t */
/* bypass ack, but still send to audio queue */
AUDIO_IPI_MSG_BYPASS_ACK = 0,
/* need ack, and block in audio queue until ack back */
AUDIO_IPI_MSG_NEED_ACK = 1,
AUDIO_IPI_MSG_ACK_BACK = 2,
/* bypass audio queue, but still send to ipc queue */
AUDIO_IPI_MSG_DIRECT_SEND = 3,
AUDIO_IPI_MSG_CANCELED = 8
};

## Slide 36
RINGBUF SW:
  DUMP_RINGBUG(LOG_F, description, rb, count)
  DUMP_RINGBUG(AUD_LOG_W, "underflow", rb, count);
RINGBUF HW
  Check funcion
  dump function
Notes: DUMP_RINGBUG
__FUNCTION__, \
description, \
(rb)->base, \
(rb)->read, \
(rb)->write, \
(rb)->size, \
audio_ringbuf_count(rb), \
audio_ringbuf_free_space(rb), \
count
-------------------------
Datacount :
R==W
R > W
W>R
Assert:
R<Base R>End
W< Base W >End

## Slide 37
IPI DMA :
  AUD_DMA_READ(scp_buf, dram_addr, size)
  AUD_DMA_WRITE(dram_addr, scp_buf, size)
    Check if in ISR
    Check scp_buf address should be 128byte aligned
  DUMP_REGION(LOG_F, description, p_region, count)
  DUMP_REGION(pr_notice, "read_idx fail", region, count);
    Dump region info as ringbuf
Notes: [I][DMA] init_audio_ipi_dma(), dma 0x6a700000, phy 0x6a700000/0x6a700000, sz 0x500000, checksum 10880/10880, offset 11008
LOG_F("%s, offset: 0x%x, size: 0x%x" \
", read_idx: 0x%x, write_idx: 0x%x" \
", region_data_count: 0x%x, count: %u", \
description, \
(p_region)->offset, \
(p_region)->size, \
(p_region)->read_idx, \
(p_region)->write_idx, \
audio_region_data_count(p_region), \
count); \